## Slide 1: Lemhi River Watershed Summary
Rob Richardson
Geomorphologist

## Slide 2
Upper Lemhi
Salmon
Baker
Lemhi
Leadore
Lower Lemhi

## Slide 3
Upper Lemhi
Lower gradient
Sinuous/meandering
Calmer water
Less gravel
Significant groundwater
High winter flows
Steeper gradient
Relatively straight
Turbulent water
More gravel
Less groundwater
High winter flows
Lower Lemhi
Salmon
Baker
Lemhi
Leadore

## Slide 4
Upper Lemhi
Lower Lemhi
Flow
Flow
Lower gradient
Sinuous/meandering
Calmer water
Less gravel
Significant groundwater
High winter flows
Steeper gradient
Relatively straight
Turbulent water
More gravel
Less groundwater
High winter flows

## Slide 5
Upper Lemhi
Lower Lemhi
Flow
Flow
Moderate flow (441 cfs at Salmon)
Moderate flow (300 cfs at Lemhi)
Lower gradient
Sinuous/meandering
Calmer water
Less gravel
Significant groundwater
High winter flows
Steeper gradient
Relatively straight
Turbulent water
More gravel
Less groundwater
High winter flows

## Slide 6
Lower Lemhi Impacts
Channel confinement/straightening
Channel simplification
Disconnected floodplain
Vegetation Removal
Levees
Riprap
Roads and development
Irrigation diversions

## Slide 7
Lower Lemhi Impacts
Channel confinement/straightening
Channel simplification
Disconnected floodplain
Vegetation Removal
Levees
Riprap
Roads and development
Irrigation diversions
Increased velocity
Greater erosion potential (lateral and vertical)
Increased flood stage
100yr
100yr

## Slide 8
Lower Lemhi Impacts
1.3 Miles
Straightened River / Abandoned Channels

## Slide 9
Flow
Lower Lemhi Impacts
Hydraulic modeling
Flow
Relatively unimpacted
Impacted
Over 6 ft/s during moderate flow
Over 12 ft/s at 1.5yr flood (777cfs)
Moderate flow (441 cfs at Salmon)
Moderate flow (300 cfs at Lemhi)

## Slide 10
Largest Recorded Floods in the Lemhi:
2,110 cfs (June 9, 1942) – Gage in Salmon (1928 – 1943)
2,920 cfs (June 6, 1995) – Gage below L5 near Salmon (1992 – 2017)
2,430 cfs (June 21, 1984) – Gage near Lemhi (1956 – 2023)
Floods
Example:
Walla Walla River
Confined Channel
100-yr Flood
1946
2020

## Slide 11
Largest Recorded Floods in the Lemhi:
2,110 cfs (June 9, 1942) – Gage in Salmon (1928 – 1943)
2,430 cfs (June 21, 1984) – Gage near Lemhi (1956 – 2023)
2,920 cfs (June 6, 1995) – Gage below L5 near Salmon (1992 – 2017)
Floods
Lower Lemhi River
1,680 cfs
Spring 2018
Barracks Ln.

## Slide 12
Wavelength
Amplitude
Belt Width = Maximum amplitude
568ft Max Amplitude in Lower Lemhi
= Minimum Meander Belt Width
Why Floodplains are Important
Allow channel space to meander
Stabilization from vegetation
Capture sediment and debris
Reduce flood energy (less erosion)
Store flood water / lower flood stage
Improve water quality

## Slide 13
Why Floodplains are Important
Allow channel space to meander
Stabilization from vegetation
Capture sediment and debris
Reduce flood energy (less erosion)
Store flood water / lower flood stage
33 Miles of the Lower Lemhi (downstream of Hayden Cr)
8,298 acres of historical floodplain
345 acres of existing floodplain (4% of historical)
Historical
Floodplain
Existing
Floodplain