## Slide 1: DEADWATER History and River Impacts

## Slide 2: Origin
Alluvial fan creates the Deadwater reach...but what caused it?
  No consensus
    Local rumors and History of the Salmon-Challis N.F.
    Army Corps reports
    Geomax report
A History of the Salmon National Forest 1973
Salmon River Ice Jams USACE 1984
Reducing Ice Jams Along the Salmon River, Geomax 1985

## Slide 3: Dump Creek
High gradient (1,000' per mile)
Highly erodible
  Challis volcanic
  Ancient lake bed up to 200' thick
Close proximity with upper Moose Creek
Drainage area ~8 square miles
Flows ~ 0.5-10 cfs
Placer and dredge mining (needed to impound water)
200'

## Slide 4: Mining Impacts
Placer mining made it impossible to determine locations of original channels
Diversion of Moose Creek into Dump Creek
  Drainage area and spring flows increased to ~33 square miles and >100 cfs (flows in excess of 400 cfs recorded)
  Downcutting created a deep chasm and undercut side slopes
    slope failures
    0.5 mile wide by 300' deep
  1974 estimates
    9,000,000 cubic yards of material transported into Salmon River
    coarser bedload deposited in alluvial fan

## Slide 5
River Impacts
Downstream deposits
Deadwater reach
Ice jam initiation
Possible increase of predatory fish
Many others (some positive)

## Slide 6
Deadwater Ice Jam
Why does it form?
  low gradient and velocity (<1ft/sec)
  highly shaded
  results in surface freezing over
    frazil ice collects underneath
    creates "hanging dam" on the upstream end
    can exceed 16' in thickness
Increased water velocity under the ice dam scours out any built up sediment within the Deadwater reach and maintains the ~19' depth
  the increased velocity and turbidity likely moves fish upstream and downstream of the Deadwater reach

## Slide 7: Ice Jam Problems
Increases river stage
Impacts many miles of river
  occasionally to upstream of Salmon
Winter flooding
Public demanded action following winter floods in 1982 and 1984
  1.0 and 1.8 million in damages
Lemhi River backed up with ice resulting in...

## Slide 12: Call for action
and studies
quickly followed...

## Slide 13: Previous work and proposed alternatives
Work prior to 1980s
  USACE
    1954
      levee construction near Salmon
    1956
      removed 12,500 cubic yards from fan
      spring flows from Dump Cr. filled in the work and even expanded the fan
  USFS – late 1970s
    restore flows into lower Moose Cr.
      eliminate transport mechanism to Salmon River
    water diversion structure / 6,000' new channel / vegetation removal from historical channel
1980s USACE Proposals
A) Channelization of Dump Creek-Deadwater (multiple proposals)
B) Levee construction along Lemhi River
C) Levee construction along Salmon River
D) Permanent floodplain evacuation
Geomax Proposal (IDFG funded)
  Spur Dikes
Rieffenberger 1991
200'
New channel
Diversion

## Slide 14: USACE Salmon River Flood Damage Reduction Project Report
Eliminated alternatives
  Levee system for Salmon, ID
  Flood proofing structures in Lemhi floodplain
  Ice barrier upstream of Salmon
  Fill the Deadwater reach
  Air-bubbler system in the Deadwater reach
  Icebreaker boat in the Deadwater reach
  Dynamite ice jams in the Deadwater area
  Heat Deadwater reach using a wood boiler
  Dusting ice cover to stimulate melting
  Diverting the Lemhi R into the old power ditch
  Spur dikes in the Deadwater reach (Geomax proposal)
low benefit to cost ratio
stranding/access
$8,000,000
Not guaranteed to eliminate ice jams
too low of water temps
lots of problems...
too large of an area
too much water/area
low sunlight/large area/rough surface
same reasons as filling the reach + higher maintenance costs – quickly dismissed
could flood new areas

## Slide 15: Considered Alternatives
Channelization of Dump Creek-Deadwater (multiple proposals)
  Full excavation
  Partial excavation and fill of Deadwater reach
  Partial excavation
  Excavation at Dump Cr and partial fill of Deadwater reach
Levee construction along Lemhi River
Levee construction along Salmon River
Permanent floodplain evacuation
  ~ 90 residences
No action
All excavation options would lower the river level and drain the upstream wetlands
Deepen existing channel around the alluvial fan and excavate material in the existing channel upstream of Deadwater
~ 375,000 cubic yards near fan and 150,000 cubic yards upstream
Channel excavation around the permiter of the fan, partial filling of the Deadwater reach, and channel excavation upstream of Deadwater
Excavation near fan: ~3,900', average depth 9', 260,000 cubic yards
~140,000 cubic yards of fill into Deadwater reach, averaging 5'
would require haul roads on both banks and a temporary bridge downstream of the fan

## Slide 16: USACE Plan Development
Draft EIS (May 1985)
IDFG pushed for fair consideration of Geomax plan
Public meetings and comment period (summer 1985)
  political (state and local) support for channelization alternative #4
  mixed public support - many comments against channelization published in final report
  no agency (federal or state) support for channelization alternative

## Slide 18: Final Selection
700 page report

## Slide 19
USACE Cold Regions Research and Engineering Laboratory
Studied ice jam formation near Salmon
Tested an experimental ice boom upstream of Salmon, ID
  reduce the amount of frazil ice making it to Deadwater
  reduce the growth of the Deadwater ice jams

## Slide 22: What now?
Status quo
  less frequent jamming
  no flooding
  little public pressure
Issues are still lurking
No easy solutions
Any attempt to alter Deadwater would likely face the same challenges
Shoup Bridge, January 2017